## Slide 1: Indoor Localization, Tracking and Navigation
Prof. Gary Chan
Department of Computer Science and Engineering
The Hong Kong University of Science and Technology
22 August 2012

## Slide 2: Project Background
  Successful outdoor Location-Based Services (LBS) based on GPS
  Many indoor LBS with important business applications or lucrative commercial potentials
  Airport
    Large, complex and irregular area
    Help tourists to
      find their departure gates after check-in
      transit flights from one gate to another
      shop or find lounges while waiting for flights
  Mall
    Help customers to find shops
    Location-based advertisement
    Etc.

## Slide 3: Meeting the Localization Challenges
Indoor localization is technically challenging
  Absence of GPS
  Lack of accurate indoor localization techniques
  Lack of a unified indoor map API
Must be beyond just “digital map”
  “smart guide”
  Help visitors to know where they are
  Direct them to go anywhere

## Slide 4: Innovating a WiFi-Based Indoor Localization System
Accurate
Low response time
High adaptability to environmental changes
    Non-intrusive to existing WiFi infrastructure
Low processing requirement (suitable for various kinds of mobile devices)
Easy to use and install
Low deployment and maintenance cost

## Slide 5: Wi-Fi Fingerprinting
Site survey
  Measure Wi-Fi signal strengths at designated points  the signature or “fingerprint” of the point
  Record these data in a database
Location lookup
  Client measures the signal strengths at its location
  Query its location based on fingerprint matching in the database
Cost
  Density of the survey points
  Frequency of the survey points
  Environmental changes
  Algorithms on fingerprint matching
  Etc.

## Slide 6: Project Scope
  To provide an accurate and efficient positioning and navigation platform
    Accurate and efficient position estimation
    Novel fusion technique on various position estimators
    Open API for spatial enquiries
  To reduce measurement overhead for WiFi-based fingerprinting
    Sparse survey points
    Environmentally adaptive

## Slide 7: Project Scope (cont.)
  To design and develop mobile app for indoor localization, tracking and navigation system
    Run in various mobile platform. (Initially Android, then iOS and others)
    Capable of:
    Locating user’s current indoor spatial location
    Determining an optimal route to the destination
    Providing real-time navigation guide
    Enabling targeted services and advertisement
    Offering easy user interface
    Plug-and-play applications through downloading

## Slide 8: Design Components and Features (I)
Core technology:
  Accurate location estimation cross multi-floors and multi-buildings
  Environmentally adaptive WiFi-based fingerprinting
  Digital map and map matching
  Optimal 3D route selection algorithm
Database data:
  Map information;
  WiFi fingerprinting measurements;
  Content data (e.g., flight info and shop promotions).

## Slide 9: Design Component and Features (II)
User experience
  Destination selection
  Navigation guidance
  Event alert
  Ads or current promotions
Managerial and monitoring
  Easy and secure installation
  Non-intrusive to existing infrastructure
  Minimum overhead to current wireless load
  LBS data analysis
  Low cost

## Slide 10: Reducing Measurements with Crowd Sourcing
WiFi-based fingerprinting
Adaptive technique to minimize labor-intensive site survey
Core Technology
Need to be frequently updated by site surveys
Dynamically updated,
Reduced site survey
Initial site survey

## Slide 11: Our Chameleon System (New)
Pruning of inaccurate APs
  Use only those unchanged signals to make location decision
Database update
  Learn the environment and adapt the signal database accordingly

## Slide 12: Simulation setup
NAP APs are placed in a circle
NREF reference points are placed in a grid with grid size g
Mobile collects and sends signal strength vector to server
Server estimates mobile’s location with a simple K-Nearest-Neighbor algorithm
(NAP, NREF, g, K) = (8, 9, 8m, 4)